## Slide 1
Bacterial and Water Quality Monitoring in the Gunpowder River
*Chichedo I. Duru1-2, Braeden Bayne2, Tristan McGregor2-3, Sophie Zuckman2,4, Steve Duker2, Theaux Le Gardeur2
1Morgan State University, Baltimore, MD, 21251;
2Gunpowder Riverkeeper, Monkton, MD, 21111;
3 Towson University, Towson, MD 21252;
4 Skidmore College, Saratoga Springs, NY 12866
Abstract
Gunpowder Riverkeeper® is a 501(c)(3) nonprofit that protects water quality, sensitive species, and community interests in the traditionally overburdened Bird, Bush, Middle, and Gunpowder River watersheds. Comprising roughly 800mi2 these watersheds host Brook Trout in the upper, forested reaches and Atlantic Sturgeon in the tidal basins. Over 1.5 million people in the Baltimore-Metro area use the Gunpowder for drinking water and many more for recreation: fishing, crabbing, boating, and swimming. 26 species of finfish use areas such as this for spawning. Gunpowder RIVERKEEPER® monitors water quality throughout the watersheds. Bacterial monitoring for Escherichia coli (E.coli) takes place at five sites using the IDEXX method. Physio-chemical parameters are measured in the tidal Gunpowder using a YSI at seven sites on dates corresponding to satellite overpasses of the Landsat-9 and Sentinel-2A to assist in “ground-truthing” for the Smithsonian Environmental Research Center (SERC) Chesapeake Water Watch Program. Six sites are monitored for quality and contamination downstream of an industrial site outfall where dissolved Oxygen and Phosphorus levels do not meet the current state standards.
Introduction
The Bird, Bush, Middle, and Gunpowder River watersheds covers roughly 800 mi2 and lead into the Chesapeake Bay
Drinking and recreational water to nearly 1.5 million residents in Baltimore Metro Area
Nursery ground for 26 species of Chesapeake Bay finfish[1].
To assess bacterial levels and water quality conditions within the Gunpowder Watershed.
Objective
Methodology
E.coli Monitoring
  IDEXX Method
  Weekly sampling during Summer Swimming Season (Memorial Day-Labor Day) in five locations
  Grab samples taken before noon
YSI Monitoring
  Samples taken to correspond to satellite overpasses
  Measurements taken in triplicates at seven sites
Chesapeake Water Watch
  CDOM, Chlorophyll A, and Turbidity measured using SERC benchtop machines with data uploaded to field scope
Gunpowder RIVERKEEPER® Territory
Results For E.coli Monitoring
Results For YSI Monitoring
Discussion
Conclusion
Acknowledgement
References
Thanks to Towson University, Skidmore College, Morgan State University for allowing their students to provide capacity to Gunpowder RIVERKEEPER® efforts in monitoring water quality in tidal and non tidal areas and providing outreach to the community.
Figure 1: Map of the territory that Gunpowder RIVERKEEPER® covers
Figure 2: Levels of E. coli in MPN
Figure 4: Results for Dissolved Oxygen (mg/L)
Figure 5: Results for Turbidity (FNU)
Recreation, fishing, and drinking water are all primary uses of the Bird, Bush, Middle, and Gunpowder River watersheds.
Large industrial presence (116 sites) in the tidal basin has prompted monitoring of water quality and the organization is seeking funding to undertake this work.
Ecosystem Impact: Bacteria levels in non-traditional swimming areas affects water quality and recreational safety
Rainfall events influence bacteria levels
Correlation may exist between DO and turbidity and needs further study.
HIGHLIGHT
During the peak of the swimming season social media impressions reached nearly 250,000 unique visitors.
* Samples collected in wet conditions.
E. Coli Analysis
Figure 3: Map of E.coli and YSI Monitoring Sites
YSI Data Collection
*
*
*
EPA 235 MPN Threshold [2]
https://gunpowderriverkeeper.org/watershed-overview/
https://mde.maryland.gov/programs/water/Beaches/Documents/factsheetepawgbeaches_jan2013rev0613.pdf
https://mde.maryland.gov/programs/water/MHB/Pages/Maryland-Healthy-Beaches-Home.aspx